## Slide 1: Radiometric Preprocessing: Atmospheric Correction

## Slide 2: “Correction” for Sun Angle Differences
 is the solar zenith angle and varies as a function of latitude, day of year, and time of day
Radiance is proportional to cos . Therefore, we can adjust for sun angle effects by:
  adjusted DN = (cos ’ / cos ) x DN
    where  = input sun angle and ’ is the normalized or reference angle (e.g., 45 degrees or  for one of several dates of imagery
Ground

Sun
Radiometric Preprocessing

## Slide 3: Haze over northeast Minnesota

## Slide 4: Effects of atmospheric scattering and absorption on spectral-radiometric responses
Effects of scattering on image quality
  Reduces contrast – dark objects are brighter, bright objects are darker
Visible bands are much more subject to atmospheric effects than infrared bands
  Sensitivity of spectral bands (high to low) to atmospheric effects
    blue, green, red, near IR, middle IR

## Slide 5: Methods for Atmospheric Correction
Atmospheric (radiative transfer) models
  Most rigorous, best, but complex
  Difficult to obtain necessary input data
Before
After
Jensen, 2007
Example of atmospheric correction with the ATCOR model

## Slide 6
Histogram adjustment
  Shifts histograms to left (to zero) under the assumption that very dark objects (0% reflectance) would be at zero if it were not for the added response due to atmospheric scattering
    i.e., the path radiance term in the remote sensing equation
  Assumes the magnitude of scattering is the same for all cover types (not exactly correct)
  Does not correct for atmospheric absorption effects

## Slide 7: Histogram Adjustment (Dark Object Subtraction)
0
255
Digital Number
Shift attributed to haze
Find pixels of dark objects that are assumed to have near zero reflectance
  Deep, clear lakes are good
Subtract their DN value from all pixels (e.g., 30)
  Has the effect of shifting the histogram to start at 0
Number of Pixels
30

## Slide 8: Histogram Adjustment (Dark Object Subtraction)
0
255
Digital Number
New histogram
Find pixels of dark objects that are assumed to have near zero reflectance
  Deep, clear lakes are good
Subtract their DN value from all pixels (e.g., 30)
  Has the effect of shifting the histogram to start at 0
Number of Pixels
30

## Slide 9: Demonstration of Image Enhancement with Image Processing Software
Spectral band combinations
Radiometric Enhancement: Contrast stretch
Spatial Enhancement: Convolution filtering
Principal Components